## Slide 1: Real-Time Time-Optimal Spacecraft Attitude Control
Author: Leonardo Eitner, M.Sc. candidate
Assistant Supervisor: Silvia Busi, PhD candidate
Head Supervisor: Prof. Dr. Marcello Romano
Context: Master’s Thesis

## Slide 2: Objectives
1st
2nd
Compute the time-optimal trajectory for any attitude maneuver
Robustly obtain solutions in less than 1 second
min(maneuver_duration)
computation_time < 1 s

## Slide 3: Methodology
1st
Compute the time-optimal trajectory for any attitude maneuver
min(maneuver_duration)
Define system dynamics →
Construct Optimal Control Problem (OCP):
  Define objective/cost function →
  Define constraints →
Choose OCP solver architecture
Legend:
→Quaternion vector
→Angular velocity vector
→Inertia matrix
→External torque vector
→Cost function
→Total maneuver duration
→Quaternion multiplication
→Cross product
→Time derivative
|||| →Euclidean norm

## Slide 4: Methodology
2nd
Robustly obtain solutions in less than 1 second
computation_time < 1 s
Choose OCP solver architecture
  Solving methods:
 | Direct | Indirect
Approach | Discretize → Optimize | Derive optimality conditions → Discretize
Robustness | Can converge even with bad initial guess | Sensitive to initial guess
Implementation | Easier | More complex
Optimality | Approximate solution | Potentially exact
Solve speed | Real-time capable | Slow

## Slide 5: Methodology
2nd
Robustly obtain solutions in less than 1 second
computation_time < 1 s
Choose OCP solver architecture
  Direct transcription methods:
 | Shooting |  | Collocation | 
 | Single | Multiple | Direct | Pseudospectral
Dynamics Handling | Forward integration | Segmented integration | Algebraic constraints | Dense global polynomial
Accuracy | Integrator-limited | Integrator-limited | Grid density dependent | Exponential (smooth problems)
Problem Size | Smallest | Medium | Large | Large
Complexity | Simplest | Moderate | Moderate-High | Highest
Robustness | Poor | Moderate | Good | Poor (non-smooth)
Real-time Suitability | Fast but unreliable | Good balance | Solver dependent | Generally slow

## Slide 6: Implementation
  Framework: CasADi
    Open-source
    Automatic differentiation
    Simple NLP interface
    Automatic c-code generation
    Source-code in c++
    Extensive NLP solver compatibility

## Slide 7: Implementation
  NLP Solvers:
 | Interior Point | SQP Methods | SCP Methods
Warm-starting | Poor | Excellent | Good
Convergence Rate | Superlinear | Superlinear | Linear to superlinear
Problem Scale | Large-scale optimal | Medium-scale optimal | Medium-scale
Robustness | Very good | Good | Moderate
Real-time Suitability | Solver dependent | Excellent | Good
Trajectory Optimization | General purpose | General purpose | Specialized strength
Example | IPOPT, Fatrop | QRSQP, SNOPT | SCPGen

## Slide 8: Implementation
  Initial guess:
    Single general initial guess
    Initial guess library
    Initial guess algorithm - PSO
A particle swarm searching for the global minimum of a function

## Slide 9: Results
  NLP Solvers:

## Slide 10: What‘s Next?
  Implement and test direct collocation
  Experiment with different solvers
  Create a Monte-Carlo simulation for robustness testing