## Slide 1: Real-Time Time-Optimal Reorientation of a Rigid Spacecraft
Author: Leonardo Eitner, M.Sc. candidate
Assistant Supervisor: Silvia Busi, PhD candidate
Head Supervisor: Prof. Dr. Marcello Romano
Context: Master’s Thesis

## Slide 2: Objectives
1st
Compute the time-optimal trajectory for any attitude maneuver
min(maneuver_duration)
3rd
Reliably obtain solutions for different boundary conditions and spacraft configurations
R_conv > 90%
2nd
Achieve computation times of less than 200ms
computation_time < 0.2 s

## Slide 3: Foundational Choices
Attitude Parameterisation
Dynamics Formulation
Optimisation Methodology
Computational Framework
NLP Solver
Control Parameterisation
BASELINE
ALGORITHM

## Slide 4
Attitude Parameterisation
Dynamics Formulation
Optimisation Methodology
Computational Framework
NLP Solver
Control Parameterisation
BASELINE
ALGORITHM
Foundational Choices
Choice:
Quaternion parameterisation
Reasoning:
No singularities
Minimal redundancy
Linear kinematic equations

## Slide 5
Attitude Parameterisation
Dynamics Formulation
Optimisation Methodology
Computational Framework
NLP Solver
Control Parameterisation
BASELINE
ALGORITHM
Foundational Choices
Choice:
Direct dynamics formulation
Reasoning:
Simpler implementation
Better handling of bang-bang control structure
Higher generality

## Slide 6
Attitude Parameterisation
Dynamics Formulation
Optimisation Methodology
Computational Framework
NLP Solver
Control Parameterisation
BASELINE
ALGORITHM
Foundational Choices
Choice:
Full trajectory parameterisation
Reasoning:
Better convergence robustness
No assumption about solution structure
Higher generality

## Slide 7
Attitude Parameterisation
Dynamics Formulation
Optimisation Methodology
Computational Framework
NLP Solver
Control Parameterisation
BASELINE
ALGORITHM
Foundational Choices
Choice:
Direct methods
Reasoning:
Less sensitive to initialisation
Less computationally expensive
Mature solver infrastructure
Intuitive initialisation

## Slide 8
Attitude Parameterisation
Dynamics Formulation
Optimisation Methodology
Computational Framework
NLP Solver
Control Parameterisation
BASELINE
ALGORITHM
Foundational Choices
Choice:
CasADi
Reasoning:
Automatic differentiation
Automatic sparsity exploitation
C-code generation
High-level interface
Compatible with multiple NLP Solvers

## Slide 9
Attitude Parameterisation
Dynamics Formulation
Optimisation Methodology
Computational Framework
NLP Solver
Control Parameterisation
BASELINE
ALGORITHM
Foundational Choices
Choice:
IPOPT
Reasoning:
General-purpose solver
Robust to bad initial guesses
Compatible with CasADi
Extensive literature validation

## Slide 10: Algorithm Optimisation
BASELINE
ALGORITHM
OPTIMISED
ALGORITHM
IPOPT VS
FATROP
CPU-RK4 VS
CVODES & GPU-RK4
Multiple Shooting VS
HS Collocation
Transcription Method
Integration Scheme
NLP Solver

## Slide 11: Algorithm Optimisation
IPOPT VS
FATROP
CPU-RK4 VS
CVODES & GPU-RK4
Multiple Shooting VS
HS Collocation
Transcription Method
Integration Scheme
NLP Solver
Multiple Shooting
HS Collocation
 | Computation Time (s) | 
 | Multiple Shooting | HS Collocation
45° | 1.265 | 7.977
90° | 0.961 | 3.974
180° | 2.512 | 4.512

## Slide 12: Algorithm Optimisation
IPOPT VS
FATROP
CPU-RK4 VS
CVODES & GPU-RK4
Multiple Shooting VS
HS Collocation
Transcription Method
Integration Scheme
NLP Solver
 | Computation Time (s) |  | 
 | CPU RK4 | GPU RK4 | GPU CVODES
45° | 15.890 | 18.129 | 852.945
90° | 2.147 | 59.575 | 3612.220
180° | 6.957 | 121.336 | 1559.010

## Slide 13: Algorithm Optimisation
IPOPT VS
FATROP
CPU-RK4 VS
CVODES & GPU-RK4
Multiple Shooting VS
HS Collocation
Transcription Method
Integration Scheme
NLP Solver
 | Computation Time (s) | 
 | IPOPT | FATROP
45° | 1.265 | 0.085
90° | 0.961 | 0.107
180° | 2.512 | 0.191

## Slide 14: Reliability Analysis
CGPOPS
LGR Collocation
IPOPT
BENCHMARK
ALGORITHM

## Slide 15: Reliability Analysis
OPTIMISED
ALGORITHM
BENCHMARK
ALGORITHM
Reference Results
Results
Compute Performance Metrics
Boundary Conditions
LHS
X 10,000

## Slide 16: Reliability Analysis
Scenario A: Symmetric spacecraft | Rest-to-Rest
Scenario B: Symmetric spacecraft | Track-to-Track
Scenario C: Asymmetric spacecraft | Track-to-Track
Benchmark
Optimised
91%
88%
70%

## Slide 17: Reliability Analysis
Benchmark
Optimised

## Slide 18: PSO Development
Legend:
→Global Best
→Personal Best
→Velocity
→Position
→Inertia weight
→Cognitive parameter
→Social parameter
→Random value
→Random Value
Update Law

## Slide 19: PSO Development
Full control trajectory parameterisation
50 x 3 + 1 = 151 dimensions
No assumption about solution structure
FULL PSO
Control switch times parameterisation
3 + 6 + 1 = 10 dimensions
Assumes bang-bang control
STO PSO

## Slide 20: PSO Reliability
MC Boundary Conditions
Compute Performance Metrics
PSO Parameters
LHS
X 1000

## Slide 21: PSO Reliability
OPTIMISED
ALGORITHM
OPTIMIZED
ALGORITHM
Results
Results
Compute Performance Metrics
Boundary Conditions
LHS
X 1000
FULL PSO
STO PSO
Initial Guess
Initial Guess

## Slide 22: PSO Development
OPTIMAL
FULL PSO
STO PSO

## Slide 23: PSO Reliability
OPTIMISED
ALGORITHM
OPTIMIZED
ALGORITHM
Results
Results
Compute Performance Metrics
Boundary Conditions
LHS
X 10,000
FULL PSO
STO PSO
Initial Guess
Initial Guess

## Slide 24: Reliability Analysis

## Slide 25: Reliability Analysis
PSO FULL
PSO STO
No PSO medians:
Scenario A: 125ms
Scenario B: 100ms
Scenario C: 295ms

## Slide 26: Reliability Analysis
PSO FULL
PSO STO
No PSO medians:
Scenario A: 125ms
Scenario B: 100ms
Scenario C: 295ms

## Slide 27: Reliability Analysis
PSO FULL
PSO STO

## Slide 28: Conclusion
 | Symmetric Spacecraft | Asymmetric Spacecraft
Computation Time | PSO STO (110ms) | No PSO (295ms)
Convergence Rate | PSO FULL (92%) | No PSO (70%)
Optimality Gap | PSO FULL (0.4%) | PSO FULL (0.9%)
Best Configuration | PSO FULL | No PSO

## Slide 29: Conclusion
 | Symmetric Spacecraft | Asymmetric Spacecraft
Computation Time | PSO STO (110ms) | No PSO (295ms)
Convergence Rate | PSO FULL (92%) | No PSO (70%)
Optimality Gap | PSO FULL (0.4%) | PSO FULL (0.9%)
Best Configuration | PSO FULL | No PSO

## Slide 30: Further Work
Incorporate flexible-body dynamics;
Add control-rate constraints to reflect actuator bandwidth limits;
Accept varying mass properties at runtime;
Develop configuration-specific and adaptive PSO tuning strategies;
Expand parameter search space beyond current 1000-case study;
Add path constraints such as keep-out cones
Hardware-in-the-loop validation

## Slide 31: The End!
I am open to questions 

## Slide 32: Algorithm Optimisation
GPU VS CPU Dynamics Propagation
  Result: CPU propagation was ~4x as fast as GPU
  Reason: Problem size is not significant to justify GPU utilization overhead (N_steps = 50)
  Conclusion: Propagate dynamics on CPU
Implicit VS Explicit Numerical Integration (CVODES VS RK4)
  Result: Although more robust, overhead from implicit integration is overwhelmingly greater
  Reason: CVODES is very heavy, even when used with CUDA
  Conclusion: Use RK4 as the numerical dynamics propagator
Fatrop vs IPOpt NLP gradient-based solvers
  Result: Fatrop is ~3x as fast as IPOpt
  Reason: Leverages problem sparsity better by being more restrictive with NLP structure
  Conclusion: Use Fatrop as the NLP gradient-based solver
CasADi automatic C-code generation VS C++
  Result: C++ was ~5x slower
  Reason: Compiled C-code is self-contained which reduces function calling overhead
  Conclusion: Generate C-code

## Slide 33: Algorithm Optimisation
GPU VS CPU Dynamics Propagation
  Result: CPU propagation was ~4x as fast as GPU
  Reason: Problem size is not significant to justify GPU utilization overhead (N_steps = 50)
  Conclusion: Propagate dynamics on CPU
Implicit VS Explicit Numerical Integration (CVODES VS RK4)
  Result: Although more robust, overhead from implicit integration is overwhelmingly greater
  Reason: CVODES is very heavy, even when used with CUDA
  Conclusion: Use RK4 as the numerical dynamics propagator
Fatrop vs IPOpt NLP gradient-based solvers
  Result: Fatrop is ~3x as fast as IPOpt
  Reason: Leverages problem sparsity better by being more restrictive with NLP structure
  Conclusion: Use Fatrop as the NLP gradient-based solver
CasADi automatic C-code generation VS C++
  Result: C++ was ~5x slower
  Reason: Compiled C-code is self-contained which reduces function calling overhead
  Conclusion: Generate C-code

## Slide 34: Results
PSO VS Fatrop NLP solvers
  PSO Results: (180 degree turn) Computation Time: 0.14s Maneuver Duration: 5s (3.24s)

## Slide 35: Results
PSO VS Fatrop NLP solvers
  Fatrop Results: (180 degree turn) Computation Time: 0.18s Maneuver Duration: 3.24s

## Slide 36: Results
PSO + Fatrop VS only Fatrop NLP solvers
  Result: PSO + Fatrop finds a solution almost always faster as only fatrop.
  Reason: Fatrop finds a solution much faster with a good initial guess
  Conclusion: PSO + Fatrop seems to be the most optimal solver configuration
 |  | Computation Time (s) |  |  | Maneuver Duration (s)
 |  | Total | Fatrop | PSO | 
Close to fixed initial guess | PSO + Fatrop | 0.16 | 0.016 | 0.15 | 3.24
 | Only Fatrop | 0.12s | 0.12 | - | 3.24
Very different from fixed initial guess | PSO + Fatrop | 0.2 | 0.03 | 0.17 | 3.44
 | Only Fatrop | 0.58 | 0.58 | - | 3.50

## Slide 37: Methodology
1st
Compute the time-optimal trajectory for any attitude maneuver
min(maneuver_duration)
Define system dynamics →
Construct Optimal Control Problem (OCP):
  Define objective/cost function →
  Define constraints →
Choose OCP solver architecture
Legend:
→Quaternion vector
→Angular velocity vector
→Inertia matrix
→External torque vector
→Cost function
→Total maneuver duration
→Quaternion multiplication
→Cross product
→Time derivative
|||| →Euclidean norm

## Slide 38: Foundational Choices
2nd
Robustly obtain solutions in less than 1 second
computation_time < 1 s
Choose OCP solver architecture
  Solving methods:
 | Direct | Indirect
Approach | Discretize → Optimize | Derive optimality conditions → Discretize
Robustness | Can converge even with bad initial guess | Sensitive to initial guess
Implementation | Easier | More complex
Optimality | Approximate solution | Potentially exact
Solve speed | Real-time capable | Slow

## Slide 39: Methodology
2nd
Robustly obtain solutions in less than 1 second
computation_time < 1 s
Choose OCP solver architecture
  Solving methods:
 | Direct | Indirect
Approach | Discretize → Optimize | Derive optimality conditions → Discretize
Robustness | Can converge even with bad initial guess | Sensitive to initial guess
Implementation | Easier | More complex
Optimality | Approximate solution | Potentially exact
Solve speed | Real-time capable | Slow

## Slide 40: Methodology
2nd
Robustly obtain solutions in less than 1 second
computation_time < 1 s
Choose OCP solver architecture
  Direct transcription methods:
 | Shooting |  | Collocation | 
 | Single | Multiple | Direct | Pseudospectral
Dynamics Handling | Forward integration | Segmented integration | Algebraic constraints | Dense global polynomial
Accuracy | Integrator-limited | Integrator-limited | Grid density dependent | Exponential (smooth problems)
Problem Size | Smallest | Medium | Large | Large
Complexity | Simplest | Moderate | Moderate-High | Highest
Robustness | Poor | Moderate | Good | Poor (non-smooth)
Real-time Suitability | Fast but unreliable | Good balance | Solver dependent | Generally slow

## Slide 41: Implementation
  Framework: CasADi
    Open-source
    Automatic differentiation
    Simple NLP interface
    Automatic c-code generation
    Source-code in c++
    Extensive NLP solver compatibility

## Slide 42: Implementation
  NLP Solvers:
 | Interior Point | SQP Methods | SCP Methods
Warm-starting | Poor | Excellent | Good
Convergence Rate | Superlinear | Superlinear | Linear to superlinear
Problem Scale | Large-scale optimal | Medium-scale optimal | Medium-scale
Robustness | Very good | Good | Moderate
Real-time Suitability | Solver dependent | Excellent | Good
Trajectory Optimization | General purpose | General purpose | Specialized strength
Example | IPOPT, Fatrop | QRSQP, SNOPT | SCPGen

## Slide 43: Implementation
  Initial guess:
    Single general initial guess
    Initial guess library
    Initial guess algorithm - PSO
A particle swarm searching for the global minimum of a function

## Slide 44: What‘s Next?
Implement and test direct collocation
Experiment with different solvers
Create a Monte Carlo simulation for robustness testing
?